## Slide 1: Controlling a UR Robot Arm inside a Custom Gazebo World
Abd alrahman alhindi

## Slide 2
Setting up ROS 2 Jazzy + Gazebo Harmonic
Following the official Gazebo Project Template Guide
Installing and running a universal robot (UR) simulation
Launching a custom world(drone race track)
Controlling the UR arm using python node
Work flow

## Slide 3
2️⃣ Setting up the Base (Gazebo + ROS 2 Template)
• I started learning Following the official Gazebo Project Template Guide tutorial.
• I learned how to link ROS 2 Jazzy with Gazebo Harmonic.
• I learned how to organize the Workspace structure which includes: worlds, robot descriptions, example apps.

## Slide 4
🧩Important Environment Setup
• Ros 2 commands come from
• gz(gazebo)commands come from
Each tool needs to be sourced before use.
ROS 2 and Gazebo “meet” through the template’s integration layer.
/opt/ros/jazzy/setup.bash
/usr/share/gz/setup.sh

## Slide 5
🚀Running ‘’World’’
• Used ros2 pkg prefix + find to locate the example world.
• Chosed the .sdf world file automatically following the command:
This will open the example ‘world’.
fWORLD=$(find "$PREFIX/share/ros_gz_example_gazebo" -name '*.sdf' | head -n1)
gz sim -r -v 4 "$WORLD"

## Slide 6
🌍Understanding What a “World” Is
• A world is a 3D simulation environment.
• Defined using SDF (Simulation Description Format).
It includes: ground plane-light-models-robots.
Each <model> in the file adds something to the environment.

## Slide 7
• Worlds stored inside packages under:
Example worlds come from:
We locate them using:
📁Where worlds live
install/<package>/share/<package>/worlds/
ros_gz_example_gazebo
ros2 pkg prefix <package>
Item | TitoDescription
World file (.sdf) | Defines environment
Model files | Robots or structures
Package prefix | Tells ROS where to look

## Slide 8
🤖Moving to Universal Robots Simulation
• Now we switch to the official UR Ros 2 gazebo simulation package.
Fully compatible with ROS 2 Jazzy + Gazebo Harmonic.
It includes:
It provides ready-to-use simulation for:
-UR3e
-UR5e
-UR10e
-Controllers.
-Launch files.
-Robot configs.

## Slide 9
📘What is the content of the package?!
• Packages are structured like a real industrial robot simulation.
The ros2 branch provides out-of-the-box support for Jazzy.
It works perfectly with created workspace.
Simulation includes:
-Joint controllers.
-Hardware interface.
-Gazebo integration plugins.
‘’This simulation used by many universities and companies.’’

## Slide 10
🏗️Building the UR Simulation
cd ~/project_ws
colcon build --symlink-install
source install/setup.bash
Sourcing install/setup.bash
let edit files inside src/ without rebuilding
Built inside the workspace to keep everything consistent
--symlink-install:
Let us edit files inside src/ without rebuilding

## Slide 11
🚀Launching the UR Simulation
ros2 launch ur_simulation_gz ur_sim_control.launch.py
Brings up joint controllers + Gazebo plugins
Loads the UR5e or UR3e or UR10e robot
Launches Gazebo Harmonic.
Confirms ROS 2 ↔ Gazebo ↔ UR bridge working properly

## Slide 12
🔗What is symlink?!
build --symlink-install
Saves a lot of time while learning and experimenting
Lets ud edit files inside src/ and see the effect immediately
Points the installation directly to the workspace files
Perfect for working on simulation configs and Python scripts
It is a pointer to another file or folder.

## Slide 13
🦾Exploring the Controller Interface
• We Verify which ROS 2 controllers are available.
• We Check active control interfaces using ROS commands:
We identify the trajectory and state controllers provided by the UR simulation.
ros2 topic list | grep joint_trajectory
ros2 control list_controllers

## Slide 14
📋Controllers we found
publishes the robot’s current joint positions
receives joint trajectory commands and moves the arm smoothly
joint_state_broadcaster
scaled_joint_trajectory_controller

## Slide 15
➡️what is scaled_joint_trajectory_controller?!
• It is the main interface for sending motion commands.
• Accepts Joint Trajectory messages
Ensures smooth, scaled, safe execution
Converts high-level motion commands → actual joint movements
This is where your Python control node will publish commands

## Slide 16
🦾Why This Controller Matters?!
• All UR motion control goes through this controller
• Python scripts must publish to:
Without this controller active, the script will not move the robot
It bridges your Python node → ROS 2 controller → Gazebo robot
/scaled_joint_trajectory_controller/joint_trajectory

## Slide 17
💻Writing Python ROS 2 Control Node
• we create Python ROS 2 node to control the UR robot.
• Published a JointTrajectory message to the controller topic
File name example: ur_rotate_demo.py

## Slide 18
🐍What the Python Node Does
• Imports rclpy
• Creates a publisher to:
Builds a JointTrajectory message
Sends target joint values to the controller
Makes the robot arm move in Gazebo
The script performs the essential ROS 2 steps:
/scaled_joint_trajectory_controller/joint_trajectory

## Slide 19
⚙️Core Python Logic
msg = JointTrajectory()
msg.joint_names = [...]
point = JointTrajectoryPoint()
point.positions = [1.5, -1.5, 1.5, -1.0, 1.5, 0.0]
point.time_from_start.sec = 6
msg.points.append(point)
pub.publish(msg)
joint_names tells the controller which joints to move
Publish → Gazebo executes the movement
positions defines the final target angles
time_from_start defines motion duration

## Slide 20
🌍Integrating a Custom Gazebo World
•we move into Integrated a custom world from the Gazebo model library
• World used: Drone Race Track.
Goal: use a world environment with UR robot simulation.
Since we are able to create a fully custom ROS 2 motion command

## Slide 21
📁Where You Placed the Custom World?!
We place the world file under:
~/project_ws/src/worlds_extra/gazebo_models_worlds_collection/worlds/
Why this location?
• Keeps third-party worlds organized
• Ensures easy access from launch files
Preserves project structure for presentations & sharing

## Slide 22
🚀Launching the Simulation with the Custom World
WORLD=~/project_ws/src/worlds_extra/gazebo_models_worlds_collection/worlds/drone_race_track_2018_actual_with_gatepapers.world
ros2 launch ur_simulation_gz ur_sim_control.launch.py world_file:=$WORLD
WORLD=
sets the full path to the world file
world_file:=
passes it into the UR launch system
Gazebo loads the world AND the UR robot together

## Slide 23
⚠️The Overlap Problem
• The robot spawned at the same position as the drone race track world.
• This caused intersection / collision at load time
This is normal when combining:
  an external world file
  with a robot that has a fixed spawn pose
Note: This happens because SDF worlds include fixed model poses

## Slide 24
🛠️Fixing the Overlap (Editing Poses)
Editing the SDF pose of the race track
Changing the <pose> values to shift models
Moving gates and objects until the robot and world no longer intersected
Understanding how Gazebo positions worlds using (x, y, z, roll, pitch, yaw)

## Slide 25
📐Automating World Adjustments
Automatically shift all gate models
2. Apply consistent offset (+3 m in X direction)
3. Regenerate a corrected world version
Note: This saved time compared to editing every SDF <pose> manually.”
We created a Python script: shift_drone_gates.py
Its purpose:

## Slide 26
🔁Automating Continuous Motion
We upgraded our Python script into a looping motion controller: ur_back_and_forth.py
It alternated between:
  Pose A (Home)
  Pose B (Rotated)
How?
  Using a timer callback
  Sending a new trajectory every few seconds
point.time_from_start = Duration(sec=2)
self.timer = self.create_timer(4.0, self.send_next_trajectory)
Robot moves to the new pose in 2 seconds
Timer triggers every 4 seconds
Creates smooth, rhythmic back-and-forth motion

## Slide 27
👀Resulting Behavior
The UR arm now moves continuously
Motion is smooth and responsive
You can see the robot cycling between poses inside the drone track

## Slide 30: Slide testuale concisa
Testo breve ed importante
  Livello 2
    Livello 3
Sottotitolo della slide
Nota a piè di pagina

## Slide 31
🧩🤖🌍Creating the Final Working Environment
We now have:
Clean drone world
UR arm placed correctly
Gazebo running smoothly
Controller active
🎯Result: The robot moved successfully inside the drone world

## Slide 32: Slide testuale concisa
Testo breve ed importante
  Livello 2
    Livello 3
Nota a piè di pagina

## Slide 33: Inserimento di un’immagine
Didascalia della foto

## Slide 34: Formattazione tabella
 | Titolo 1 |  |  | 
Titolo A | Contenuto |  |  | 
Note | Nota 1 |  |  | 

## Slide 35: Immagine e testo
Didascalia esplicativa dell’immagine

## Slide 36: Immagine e testo
Didascalia esplicativa dell’immagine

## Slide 37: Slide a due sezioni
Testo sezione 1
Testo sezione 2
Sezione 1
Sezione 2

## Slide 38: Slide a 3 sezioni
Testo sezione 1
Testo sezione 2
Testo sezione 3
Sezione 1
Sezione 2
Sezione 3

## Slide 39: Slide riassuntiva per punti
Sottotitolo della slide
Punto 1
Punto 2
Punto 3